## Slide 1: NIC - Are all they all the same and Why?
By Ethan Yu

## Slide 2: Why is a NIC card needed? What is it's function? Is there a difference between them?
Working as an interface at the TCP/IP layer.
NIC card is able to transmit signals at the physical layer and deliver data packets at the network layer.
Acts as a middleman between a computer/server and a data network.

## Slide 3: Identify the three common types of Network interfaces available today for consumers?
Network interface cards
motherboard-down
USB network adapters

## Slide 4: Explain how these three different types are different? Advantages and disadvantages of each.
motherboard-down
Advantages:
Motherboard-down controllers allows you to provide networking services without the use of an expansion slot
Usually less expensive than an add-in card,
Disadvantages:
Utilize processor power to encode and decode data through the network layers.
Wired USB adapters
Advantages:
Provides portable and quick installation for network connections that can be installed by individuals of any skill level.
Ease of use the ability to add a connection without requiring a motherboard change or filling one of its slots.
Disadvantages:
- USB is traditionally slower than the quickest Ethernet links, causing potential bottlenecks when network performance exceeds 50 Mb/s using USB 2.0. USB 3.0 should alleviate that.

## Slide 5: Explain how these three different types are different? Advantages and disadvantages of each.
Network interface cards
Advantages:
Handle the buffer storage, encoding and decoding of data through the seven network layers. Ease of use the ability to add a connection without requiring a motherboard change or filling one of its slots.
Typically, there are more advanced feature sets available on network interface cards, as they have dedicated storage and the processing to support this without affecting the CPU.
Disadvantages:
An installed NIC will take one of your motherboard expansion slots, which can be troublesome if you are running several add-on components in a small form factor computer.

## Slide 6: How many ports do Household vs Business NiCs have? What kind of ports are they for household vs business?
Can’t find specific amount but I think the business NIC’s would have maybe 4 ports, and for household 2 ports.

## Slide 7: What is Networking Bonding and why is it used?
Process of combing 2 or more network interfaces together into one interface.
Offers performance improvements
If the active NIC goes down, another NIC becomes active

## Slide 8: Identify all existing PC slots standards used? (Legacy & New)
PCI = Network card, SCSI, Sound card, Video card
PCI Express = Video card
AGP = Video card
ISA = Network card, Sound card, Video card
AMR = Modem, Sound card
CNR = Modem, Network card, Sound card
EISA = SCSI, Network card, Video card
VESA = Video card

## Slide 9: Explain the anatomy of a standard NIC
A NIC provides a computer with a dedicated, full-time connection to a network.
Implements the physical layer circuitry necessary for communicating with Ethernet or Wi-Fi.
Each card represents a device and can prepare, transmit and control the flow of data a network.

## Slide 10: Provide an explanation of how and why Nic involves Parallel to Serial Data to connect to computers. (See diagram below)-
Both serial and parallel transmissions have advantages and disadvantages.
Parallel transmission is used for short distances and provides greater speed.
Serial transmission is reliable for transferring data over long distances.

## Slide 11: END
By Ethan Yu